## Slide 1: Driver Distraction Detection
Real-Time Driver Monitoring Using Laptop Webcam
Presented by: Phani Sri Morampudi , Ahalya Rani Gowra
Date: 14 – 08 - 2025

## Slide 2: Project Overview
• Monitors driver's attention in real-time
• Detects eye closure, head movements, mobile usage, and side mirror checking
• Provides timely alerts to enhance driving safety

## Slide 3: Objectives
• Detect driver distraction using EAR and head orientation
• Implement three-stage alert system
• Differentiate between mobile and Bluetooth usage
• Provide visual feedback for driver status

## Slide 4: System Components
Software Components:
• Python 3.11.9
• Libraries: OpenCV, MediaPipe, NumPy, Pygame
Features:
Eye & Face Detection
Distraction Detection
Mobile Usage Detection
Three-Stage Alerts

## Slide 5: Eye Aspect Ratio (EAR)
• Monitors eye closure using landmarks
• Formula:
• EAR below threshold triggers distraction detection
EAR = (||p2 - p6|| + ||p3 - p5||) / (2 * ||p1 - p4||)

## Slide 6: Head Orientation
• Nose tip relative to eye centers determines head turn
• Detects side mirror checking
• Ignored if less than 10 seconds to avoid false alerts

## Slide 7: Alert System
• Stage 1 (20 sec): Air flow + water spray simulation
• Stage 2 (25 sec): Vibrating seat simulation
• Stage 3 (30 sec): Sound alert simulation
• Mobile usage triggers immediate alert

## Slide 8: Visual Feedback
• Green dots for detected eyes
• Status Messages:
• Focused
• Distracted
• Checking Side Mirror
• Using Mobile
• Provides real-time visual indication

## Slide 9: Implementation Highlights
• Real-time webcam feed processing
• Eye closure detection using EAR
• Head direction and gaze tracking
• Stage-based alert system with sound and visual notifications

## Slide 10: How to Run
Install Python 3.11.9
Install libraries:
• pip install opencv-python mediapipe numpy pygame
3. Place alert sound files in project folder
4. Run script:
• python driver_monitoring.py
5. Press q to quit

## Slide 11: Observations
• Accurate detection of eye closure and distractions
• Stage-based alerts effective
• Mobile usage detection functional
• Side mirror checks ignored for 10 seconds

## Slide 12: Future Improvements
• YOLO integration for accurate mobile detection
• Real-time Bluetooth headset detection
• Hardware alert integration for embedded platforms (Jetson Nano)